## Slide 1: 15CSE301 Computer Organization and Architecture
Datapath
Dr Ganesh Neelakanta Iyer
Amrita Vishwa Vidyapeetham, Coimbatore
Associate Professor, Dept of Computer Science and Engg
Reference:
Chapter 4 – 4.1 -4.4
Computer Organization and Design, The hardware / software interface, 4rd Edition

## Slide 2: RECAP
You have learnt MIPS architecture
  Instruction set
  Addressing Modes
  Conversion of instructions to different formats

## Slide 3: Next
Explanation of the principles and techniques used in implementing a processor, starting with a highly abstract and simplified overview
Then a section that builds up a datapath and constructs a simple version of a processor sufficient to implement an instruction set like MIPS

## Slide 4: First
Implementation that includes a subset of the core MIPS instruction set:
  The memory-reference instructions load word (lw) and store word (sw)
  The arithmetic-logical instructions add, sub, AND, OR, and slt
  The instructions branch equal (beq) and jump (j), which we add last

## Slide 5: Overview of implementation
For every instruction, the first two steps are identical:
  Send the program counter (PC) to the memory that contains the code and fetch the instruction from that memory.
  Read one or two registers, using fields of the instruction to select the registers to read. For the load word instruction, we need to read only one register, but most other instructions require that we read two registers

## Slide 6: Overview of implementation
After these two steps, the actions required to complete the instruction depend on the instruction class
Fortunately, for each of the three instruction classes (memory-reference, arithmetic-logical, and branches), the actions are largely the same, independent of the exact instruction
The simplicity and regularity of the MIPS instruction set simplifies the implementation by making the execution of many of the instruction classes similar

## Slide 7: Overview of implementation
For example, all instruction classes, except jump, use the arithmetic-logical unit (ALU) after reading the registers
The memory-reference instructions use the ALU for an address calculation, the arithmetic-logical instructions for the operation execution, and branches for comparison
After using the ALU, the actions required to complete various instruction classes differ

## Slide 8: Overview of implementation
A memory-reference instruction will need to access the memory either to read data for a load or write data for a store
An arithmetic-logical or load instruction must write the data from the ALU or memory back into a register
Lastly, for a branch instruction, we may need to change the next instruction address based on the comparison; otherwise, the PC should be incremented by 4 to get the address of the next instruction

## Slide 9: An abstract view of the implementation of the MIPS subset showing the major functional units and the major connections between them

## Slide 10: Implementing MIPS: the Fetch/Execute Cycle
High-level abstract view of fetch/execute implementation
  use the program counter (PC) to read instruction address
  fetch the instruction from memory and increment PC
  use fields of the instruction to select registers to read
  execute depending on the instruction
  repeat…

## Slide 11: Overview: Processor Implementation Styles
Single Cycle
  perform each instruction in 1 clock cycle
  clock cycle must be long enough for slowest instruction; therefore,
  disadvantage: only as fast as slowest instruction
Multi-Cycle
  break fetch/execute cycle into multiple steps
  perform 1 step in each clock cycle
  advantage: each instruction uses only as many cycles as it needs
Pipelined
  execute each instruction in multiple steps
  perform 1 step / instruction in each clock cycle
  process multiple instructions in parallel – assembly line

## Slide 12: Functional Elements
Two types of functional elements in the hardware:
  elements that operate on data (called combinational elements)
  elements that contain data (called state or sequential elements)

## Slide 13: Combinational Elements
Works as an input  output function, e.g., ALU
Combinational logic reads input data from one register and writes output data to another, or same, register
  read/write happens in a single cycle – combinational element cannot store data from one cycle to a future one
Combinational logic hardware units

## Slide 14: State Elements
State elements contain data in internal storage, e.g., registers and memory
All state elements together define the state of the machine
  What does this mean? Think of shutting down and starting up again…
Flipflops and latches are 1-bit state elements, equivalently, they are 1-bit memories
The output(s) of a flipflop or latch always depends on the bit value stored, i.e., its state, and can be called 1/0 or high/low or true/false
The input to a flipflop or latch can change its state depending on whether it is clocked or not…

## Slide 15: State Elements on the Datapath: Register File
Registers are implemented with arrays of D-flipflops
Register file with two read ports and one write port
Clock
5 bits
5 bits
5 bits
32 bits
32 bits
32 bits
Control signal

## Slide 16: State Elements on the Datapath: Register File
Port implementation:
Read ports are implemented with a pair of multiplexors – 5 bit multiplexors for 32 registers
Write port is implemented using a decoder – 5-to-32 decoder for 32 registers. Clock is relevant to write as register state may change only at clock edge
Clock
Clock

## Slide 17: Building a datapath
Address
Address
Program Counter
The PC is a state element that holds the address of the current instruction
A 32-bit register which holds the instruction address and is updated at the end of every clock cycle
Normally PC increments sequentially except for branch instructions
The arrows on either side indicate that the PC state element is both readable and writeable

## Slide 18: Building a datapath
Instruction Memory
Instruction memory is a state element that provides read-access to the instructions of a program and, given an address as input, supplies the corresponding instruction at that address

## Slide 19: Building a datapath
Adder
The adder is responsible for incrementing the PC to hold the address of the next instruction
It takes two input values, adds them together and outputs the result.

## Slide 20: Single-cycle Implementation of MIPS
We first implement MIPS using a single long clock cycle for every instruction
Every instruction begins on one up (or, down) clock edge and ends on the next up (or, down) clock edge
This approach is not practical as it is much slower than a multicycle implementation where different instruction classes can take different numbers of cycles
  in a single-cycle implementation every instruction must take the same amount of time as the slowest instruction
  in a multicycle implementation this problem is avoided by allowing quicker instructions to use fewer cycles
Even though the single-cycle approach is not practical it is simple and useful to understand first
Note : we shall implement jump at the very end

## Slide 21: Datapath: Instruction Store/Fetch & PC Increment
Three elements used to store and fetch instructions and increment the PC
Datapath

## Slide 22: Datapath
Fetch the instruction at the address in PC
Decode the instruction
Execute the instruction
Update the PC to hold the address of the next instruction
Note: we perform PC+4 because MIPS instructions are word-aligned

## Slide 23: Animating the Datapath
Instruction <- MEM[PC]
PC <- PC + 4

## Slide 24: RECAP: R-Type instructions
Used for arithmetic, logical, shift instructions
  op: Basic operation of the instruction (opcode)
  rs: first register source operand
  rt: second register source operand
  rd: register destination operand
  shamt: shift amount
  funct: function - specific type of operation
Also called “R-Format” or “R-Type” Instructions
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
0
31

## Slide 25: Building a datapath
ALU
The ALU performs the operation indicated by the instruction
It takes two operands, as well as a 4-bit wide operation selector value
The result of the operation is the output value
We have an additional output specifically for branching – we will cover this later
32
32
32

## Slide 26: Building a datapath
Register File
To support R-format instructions, we’ll need to add a state element called a register file
A register file is a collection readable/writeable registers
  Read register 1 – first source register. 5 bits wide
  Read register 2 – second source register. 5 bits wide
  Write register – destination register. 5 bits wide
  Write data – data to be written to a register. 32 bits wide.

## Slide 27: Building a datapath
Register File
At the bottom, we have the RegWrite input
A writing operation only occurs when this bit is set
The two output ports are:
  Read data 1 – contents of source register 1
  Read data 2 – contents of source register 2

## Slide 28: Datapath: R-Type Instruction
Two elements used to implement
R-type instructions
Datapath

## Slide 29: Animating the Datapath
add rd, rs, rt
R[rd] <- R[rs] + R[rt];

## Slide 30: RECAP: I-type instructions
Used for load, store instructions
  op: Basic operation of the instruction (opcode)
  rs: first register source operand
  rt: second register source operand
  offset: 16-bit signed address offset (-32,768 to +32,767)
Also called “I-Format” or “I-Type” instructions
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
Address

## Slide 31: Building a datapath
Data Memory
The data memory element implements the functionality for reading and writing data to/from memory
There are two inputs. One for the address of the memory location to access, the other for the data to be written to memory if applicable.
The output is the data read from the memory location accessed, if applicable
Reads and writes are signaled by MemRead and MemWrite, respectively, which must be asserted for the corresponding action to take place

## Slide 32: Building a datapath
Sign extension unit
To perform sign-extending, we can add a sign extension element
The sign extension element takes as input a 16-bit wide value to be extended to 32-bits
To sign extend, we simply replicate the most-significant bit of the original field until we have reached the desired field width

## Slide 33: Datapath: Load/Store Instruction
Two additional elements used
To implement load/stores
Datapath

## Slide 34: Animating the Datapath
lw rt, offset(rs)
R[rt] <- MEM[R[rs] + s_extend(offset)];

## Slide 35: Animating the Datapath
sw rt, offset(rs)
MEM[R[rs] + sign_extend(offset)] <- R[rt]

## Slide 36: Datapath: Branch Instruction
Datapath
No shift hardware required:
simply connect wires from
input to output, each shifted
left 2 bits

## Slide 37: Animating the Datapath
beq rs, rt, offset
  if (R[rs] == R[rt]) then PC <- PC+4 + s_extend(offset<<2)

## Slide 38: MIPS Datapath I: Single-Cycle
Input is either register (R-type) or sign-extended
lower half of instruction (load/store)
Combining the datapaths for R-type instructions
and load/stores using two multiplexors
Data is either
from ALU (R-type)
or memory (load)

## Slide 39: Animating the Datapath: R-type Instruction
add rd,rs,rt

## Slide 40: Animating the Datapath: Load Instruction
lw rt,offset(rs)

## Slide 41: Animating the Datapath: Store Instruction
sw rt,offset(rs)

## Slide 42: MIPS Datapath II: Single-Cycle
Adding instruction fetch
Separate instruction memory
as instruction and data read
occur in the same clock cycle
Separate adder as ALU operations and PC
increment occur in the same clock cycle

## Slide 43: MIPS Datapath III: Single-Cycle Versatile Datapath
Adding branch capability and another multiplexor
Instruction address is either
PC+4 or branch target address
Extra adder needed as both
adders operate in each cycle
New multiplexor
Important note: in a single-cycle implementation data cannot be stored
during an instruction – it only moves through combinational logic
Question: is the MemRead signal really needed?! Think of RegWrite…!

## Slide 44: Datapath Executing add
add rd, rs, rt

## Slide 45: Datapath Executing lw
lw rt,offset(rs)

## Slide 46: Datapath Executing sw
sw rt,offset(rs)

## Slide 47: Datapath Executing beq
beq r1,r2,offset

## Slide 48: Control
Now we have a complete datapath for our simple MIPS subset – we will show the whole diagram in just a couple of minutes. Before that, we will add the control.
The control unit is responsible for taking the instruction and generating the appropriate signals for the datapath elements
Signals that need to be generated include
  Operation to be performed by ALU.
  Whether register file needs to be written.
  Signals for multiple intermediate multiplexors.
  Whether data memory needs to be written.
For the most part, we can generate these signals using only the opcode and funct fields of an instruction

## Slide 49: Control signals

## Slide 50
Office Hours
  Monday 1120-1210 @ My office

## Slide 51: RECAP: J-Type Instructions
J instructions have the following machine-code format:
opcode | Pseudo-Address
6 bits | 26 bits
Opcode
  The 6 bit opcode corresponding to the particular jump command. (26 to 31)
Address
  A 26-bit shortened address of the destination. (0 to 25)
  The two least significant bits are removed, and the 4 most significant bits are removed, and assumed to be the same as the current instruction's address

## Slide 52: Datapath for J format
j targetaddress

## Slide 53: ALU Control Lines
Note here that the ALU has a 4-bit control line called ALU operation
The first two bits indicate whether a and b need to be inverted, respectively.
The last two bits indicate the operation

## Slide 54: ALU Control Lines
How do we set these control lines? Consider the control unit below.
The 2-bit ALUop input indicates whether an operation should be add (00) for loads and stores, subtract (01) for beq, or determined by the funct input (10)
  Case 00 and 01 are determined by the op field
  Case 10 is used by R-format instructions
The 6-bit Funct input corresponds to the funct field of R-format instructions. Each unique funct field corresponds to a unique set of ALU control input lines

## Slide 55: ALU Control Lines

## Slide 57: Datapath with Control II
MIPS datapath with the control unit: input to control is the 6-bit instruction
opcode field, output is seven 1-bit signals and the 2-bit ALUOp signal

## Slide 58: Control signals
From the previous slide, we can see that the control signals are chosen based on the upper 6 bits of the instruction. That is, the opcode is used to set the control lines
Furthermore, as we saw before, the ALU control input lines are also dictated by the funct fields of applicable instructions.

## Slide 59: Datapath with Control II (cont.)
Determining control signals for the MIPS datapath based on instruction opcode
PCSrc cannot be
set directly from the
opcode: zero test
outcome is required

## Slide 60: Control Signals: R-Type Instruction
Control signals
shown in blue
1
0
0
0
1
???
Value depends on funct
0
0

## Slide 61: Control Signals: lw Instruction
0
Control signals
shown in blue
0
010
1
1
1
0
1

## Slide 62: Control Signals: sw Instruction
0
Control signals
shown in blue
X
010
1
X
0
1
0

## Slide 63: Control Signals: beq Instruction
Control signals
shown in blue
X
110
0
X
0
0
0
1 if Zero=1

## Slide 64: Datapath with Control III
31-26
25-0
opcode
address
Jump
MIPS datapath extended to jumps: control unit generates new Jump control bit
New multiplexor with additional
control bit Jump
Composing jump
target address

## Slide 65: Datapath Executing j

## Slide 66: R-type Instruction: Step 1 add $t1, $t2, $t3 (active = bold)
Fetch instruction and increment PC count

## Slide 67: R-type Instruction: Step 2 add $t1, $t2, $t3 (active = bold)
Read two source registers from the register file

## Slide 68: R-type Instruction: Step 3 add $t1, $t2, $t3 (active = bold)
ALU operates on the two register operands

## Slide 69: R-type Instruction: Step 4 add $t1, $t2, $t3 (active = bold)
Write result to register

## Slide 70: Load Instruction Steps lw $t1, offset($t2)
Fetch instruction and increment PC
Read base register from the register file: the base register ($t2) is given by bits 25-21 of the instruction
ALU computes sum of value read from the register file and the sign-extended lower 16 bits (offset) of the instruction
The sum from the ALU is used as the address for the data memory
The data from the memory unit is written into the register file: the destination register ($t1) is given by bits 20-16 of the instruction

## Slide 71: Load Instruction lw $t1, offset($t2)

## Slide 72: Branch Instruction Steps beq $t1, $t2, offset
Fetch instruction and increment PC
Read two register ($t1 and $t2) from the register file
ALU performs a subtract on the data values from the register file; the value of PC+4 is added to the sign-extended lower 16 bits (offset) of the instruction shifted left by two to give the branch target address
The Zero result from the ALU is used to decide which adder result (from step 1 or 3) to store in the PC

## Slide 73: Branch Instruction beq $t1, $t2, offset

## Slide 74: Single-cycle Implementation Notes
The advantage of single cycle implementation is that it is simple to implement.
Disadvantages
  The clock cycle will be determined by the longest possible path, which is not the most common instruction. This type of implementation violates the idea of making the common case fast.
  May be wasteful with respect to area since some functional units, such as adders, must be duplicated since they cannot be shared during a single clock cycle